# GENERAL RULES

# Back

- ALL TRACK OFFICALS DECISIONS FINAL ON ANY POINT OF

CONTROVERSY , ANY DISAGREEMENT WILL RESULT IN DISQUALIFICATION. VULGAR LANGUAGE OR USE OF ALCOHOLIC

BEVERAGES WILL BE GROUNDS FOR DISMISSAL AND DISQUALIFICATION.

- TRACTORS SHALL BE TWO (2) WHEEL DRIVE ONLY.

# EACH TRACTOR MUST RUN ITS RESPECTIVE CLASS.

- TIRES:

# STOCK: TURF TIRES ONLY, NO CUTTING

# MODIFIED: 26X12X12, CUTTING ALLOWED

SUPER MODIFIED: 31X15.50X15 MAX. CUTTING ALLOWED

OPEN: 31X15.50X15 MAX. CUTTING ALLOWED

- DRAWBAR: AT LEAST 6 INCHES FROM THE CENTER OF REAR TO HOOKING POINT.

# RIGIDLY MOUNTED IN ALL DIRECTIONS. UPPER EDGE OF HOOKING SURFACE

SHALL BE NO MORE THAN 13 INCHES FROM THE GROUND. A MINIMUM OF A

1 ½ INCH HOLE SHALL BE PROVIDED FOR HOOK ATTACHMENT. NO CLEVISES

OR BALLS.

- ALL TRACTORS SHALL BE EQUIPPED WITH WHEELIE BARS STRONG ENOUGH TO

# SUPPORT TRACTOR AND DRIVER WITH REAR WHEELS SUSPENDED IN AIR.

# GROUND CONTACT POINT SHALL BE A MINIMUM OF 6 INCHES BEHIND REAR

TIRES AND NO MORE THAN 6 INCHES FROM GROUND.

- NO PORTION OF THE TRACTOR SHALL INTERFERE WITH THE SLED OR HITCHING

# MECHANISM AT ANY TIME. WHEELIE BAR MUST NOT TOUCH HOOK UP CHAIN

- ALL WEIGHTS SHALL BE MADE OF SOLID CONSTRUCTION. WEIGHTS MUST BE

# SECURED TO TRACTOR. NO SITTING ON WEIGHTS. WEIGHT BAR MUST NOT

EXTEND MORE THAN 2 INCHES BEYOND WIDEST PORTION OF TRACTOR OR

TIRES. ANYTHING COMING OFF TRACTOR DURING PULL WILL BE CAUSE FOR

DISQUALIFICATION. ONCE A PULLER HAS BEEN SIGNALED TO STOP, THE PULL

IS OVER. ANYTHING FALLING OFF AFTER THE SIGNAL, WILL NOT BE DIS-

QUALIFIED.

- FRAME ALTERATIONS ARE ALLOWED EXCEPT STOCK. MODIFIED WHEELBASE IS

# NOT TO EXCEED 60 INCHES CENTER TO CENTER. SUPER MODIFIED: NO WHEEL

BASE LIMIT, EXCEPT IT’S NOT TO EXCEED 8 FEET IN LENGTH.

9.    ALL TRACTORS SHALL BE EQUIPPED WITH WORKING BRAKES. TRACTOR SHOULD

# BE ABLE TO DRIVE TO THE SLED INDER ITS OWN POWER.

10.    ALL TRACTORS SHALL HAVE A RIGIDLY MOUNTED SEAT.

11.    ALL DRIVESHAFTS, PULLEYS, OR SPROCKETS SHALL HAVE A SAFETY COVER.

12.    SUPER MODIFIED, OPEN, AND OUTLAW SHALL HAVE FUNCTIONAL BREAKAWAY

# SWITCHES.

- ALL EXHAUST PIPES SHOULD BE IN AN UPWARD POSITION AT LEAST 10 DEGREES

# ABOVE A HORIZONTAL POSITION.

- ALL MODIFIED STOCK, PRO MODIFIED CLASSES SHALL START UNDER ITS OWN

# POWER WITHOUT A REMOTE STARTER. PULL CORDS AND JUMPER CABLES ARE

ACCEPTABLE. THIS DOES NOT APPLY TO SUPER MODIFIED OR OPEN CLASSES.

- HELMETS MUST BE WORN IN PULLS, MUST BE DOT APPROVED MOTORCYCLE TYPE

# HELMET WITH CHIN STRAP AND IT STRAPPED. (SPECIAL MEDICAL PROBLEMS,

CONTACT TRACK HEADQUARTERS)

- IF ANYONE HAS OR SEES A PROBLEM, NOTIFY TRACK MANAGER IMMEDIATELY.

- ALL TRACKS MUST HAVE FIRE EXTINGUISHERS ON TRACK.