# Back

# SUPER STOCK					SUPER STOCK

# 950 LB.						950 LB.

1& 2 CYLINDER FLAT HEAD			1 & 2 CYLINDER OHV

32.9 CI OR LESS					32.9 CI OR LESS

SUPER STOCK					SUPER STOCK

1050 LB.						1050 LB.

1 & 2 CYLINDER FLATHEAD			1 & 2 CYLINDER OHV

33-50 CI						33-50 CI

# ENGINE:     ANY ONE OR TWIN CYLINDER FLAT HEAD WITH 32.9 CI OR LESS.

# OUTSIDE APPEARANCE OF ENGINE SHOULD APPEAR STOCK

WITH SHEET METAL FROM FACTORY. ENGINE INTAKE AND

EXHAUST CAN BE PORTED.

# STD. BORE: CAN BE BORED OUT TO FACTORY OVERBORE SIZES.

# STD. PISTON: SAME TYPE AS CAME FROM FACTORY. NO

# MODIFICATIONS.

# STD. STROKE: NO MODIFICATION. PISTON CANNOT EXCEED DECK

# LEVEL.

# STD. VALVES: STOCK SIZE.

# STD. HEADS: CAN BE SHAVED.

# STD. FLYWHEELS & STARTERS: MAY HAVE PULL START. MUST BE

# ORIGINAL TYPE STARTER. CAN HAVE STEEL FLYWHEEL WITH

# SAME WEIGHT AND DIAMETER AS ORIGINAL

# STD. IGNITION: SYSTEM AS IT CAME, CAN BE CONVERTED TO FACTORY

# ELECTRONIC IGNITION

# CAMSHAFTS: MAX. LIFT .400 (TO COVER ALL BRANDS OF ENGINES) WE

# WILL NOT CHECK DURATION, BUT NO ADJUSTABLE CAMS.

# MUST BE 1 PIECE CAM. CAM LIFT WILL BE CHECKED AT VALVE.

# CARBURATORS: MUST BE STD. TYPE CARBURATOR THAT CAME ON

# YOUR ENGINE WHEN NEW. CARB CAN BE BORED OUT,

# REJETTED, ETC.

# FUEL:        GASOLINE, METHONOL, OR MIXED, NO PRESSURIZED FUEL

# SYSTEMS OF ANY KIND.

WHEELS:   MAX. DIA. OF 12 INCHES    MAX. WIDTH OF 12 INCHES.

TIRES:        26X12.00X12 MAX. SIZE. NO SPECIALTY PULLING TIRES.

# THROTTLE:  TRACTOR MUST BE EQUIPPED WITH A SPRING LOADED

(DEADMAN) THROTTLE.

# DRIVES:     MODIFICATIONS CAN BE MADE. MAX WIDTH ACROSS BACK OF

# TIRES-48 INCHES, MEASURED OUTSIDE OF TIRE.

# HITCHES:  MUST NOT BE OVER 13 INCHES HIGH FROM GROUND. HITCH

# HOLE MUST BE 1 ½ INCHES ROUND, NO CLEVISES. HITCH MUST

RIGID AND NOT MOVE SIDE TO SIDE OR UP AND DOWN. ALL

EXTRA HITCH HOLES MUST BE PLUGGED OFF AT PULL TIME SO

SLED CAN BE HOOKED IN CORRECT HOLE.

# WHEELIE BARS: TRACTOR SHOULD BE EQUIPPED WITH WHEELIE BARS

# STRONG ENOUGH TO SUPPORT TRACTOR WITH DRIVER ON

BOARD WITH REAR WHEELS OFF THE GROUND. GROUND

CONTACT SHOULD BE AT LEAST 6 INCHES FROM OUTERMOST

PART OF TIRE, BUT NOT MORE THAN 6 INCHES OFF GROUND.

# NO PORTION OF TRACTOR OR WHEELIE BAR SHOULD TOUCH

# HOOKING CHAIN WHEN CHAIN IS TIGHT.

# FRAME:     ALTERATIONS ARE ALLOWED. WHEELBASE NOT TO EXCEED 60

# INCHES CENTER TO CENTER. 8 FEET TOTAL LENGTH OF

TRACTOR MEASURED FROM BACK OF REAR TIRE TO ANYTHING

IN FRONT OF TRACTOR. WHEELIE BARS ARE NOT INCLUDED IN

THIS MEASUREMENT.

# HOOD & GRILL: REQUIRED, BUT CAN BE FABRICATED. ALL MOVING PARTS

# SHOULD BE COVERED.

# AGE:          SUPER STOCK 950 CLASSES: AGES 8 YEARS OLD AND UP

# SUPER STOCK 1050 CLASSES: AGES 12 YEARS OLD AND UP