# Back

# PURE STOCK                                  PURE STOCK

# 950 LB.  				1050 LB.

1 & 2 CYLINDER			1 & 2 CYLINDER

32.9 CI OR LESS			33-50 CI

# ENGINE:    COMPLETELY STOCK ENGINES, NO MODIFICATIONS ON

# ENGINE. NO FACTORY FUEL INJECTION, NO ELECTRIC

# FUEL PUMPS.

MUFFLER: CAN HAVE MUFFLERS OR STRAIGHT PIPE, STRAIGHT PIPES

# MUST POINT UP. EXHAUST OF MUFFLER CANNOT BLOW DOWN.

# CARBURATOR:  CARBURATOR WILL BE STOCK WITH STOCK PARTS.

# NO MODIFICATION.

# FUEL:        GASOLINE ONLY.

# WHEELS:  12-INCH DIA. MAX.  12-INCH WIDE MAX.  NO DUALS.

# TIRES:       26X12.00X12 MAX.  TURF TIRES, NO CUTTING.

# THROTTLE:  TRACTORS SHOULD BE EQUIPPED WITH A SPRING LOADED

(DEADMAN) THROTTLE.

# DRIVES:    NO MODIFICATIONS. WIDTH ACROSS BACK OF TIRES, 48 INCHES.

# GOVERNORS: REQUIRED. MAX. RPM=4000.

# HITCHES: MUST NOT BE OVER 13 INCHES HIGH FROM GROUND, AT LEAST

# 6 INCHES FROM CENTERLINE OF AXLE. HOLE MUST BE 1 ½

INCHES ROUND, NO CLEVISES. HITCH MUST BE RIGID AND NOT

MOVE SIDE TO SIDE OR UP AND DOWN. ALL EXTRA HITCH HOLES

MUST BE PLUGGED OFF AT PULL TIME SO SLED CAN BE HOOKED

IN CORRECT HOLE.

# WHEELIE BARS:  TRACTOR SHOULD BE EQUIPPED WITH WHEELIE BARS

# STRONG ENOUGH TO SUPPORT TRACTOR WITH DRIVER ON

BOARD WITH REAR WHEELS OFF THE GROUND. GROUND

CONTACT SHOULD BE AT LEAST 6 INCHES FROM OUTER-

MOST PART OF TIRE, BUT NOT MORE THAN 6 INCHES OFF

GROUND. NO PORTION OF TRACTOR OR WHEELIE BAR SHOULD

TOUCH HOOKING CHAIN WHEN CHAIN IS TIGHT.

# FRAME:    NO ALTERATIONS ARE ALLOWED. WHEELBASE SHOULD BE

# STOCK. 8 FEET TOTAL LENGTH OF TRACTOR MEASURED FROM

BACK OF REAR TIRE TO ANYTHING IN FRONT OF TRACTOR.

# WHEELIE BARS ARE NOT INCLUDED IN THIS MEASUREMENT.

# HOOD & GRILL:  REQUIRED, BUT CAN BE FABRICATED. ALL MOVING

# PARTS SHOULD BE COVERED.

# AGE:          8 YEARS OLD AND UP