Back

# OPEN

# 1050 LB

# ENGINE:     ANY 1 CYLINDER OR TWIN CYLINDER, 2 CYCLE OR 4 CYCLE,

# DIESEL/ CUSTOM BLOCKS, OR TWO CYLINDER MOTORCYCLE

# ENGINES AT 750 CC.

# SAFETY SHIELD: 1/8 INCH THICK STEEL OR ¼ INCH ALUMINUM COVERING

# FLYWHEEL.

# FUEL:          GASOLINE, METHONOL, OR MIXED, NITROUS OXIDE

# INTAKE SYSTEM: ANY CARBURATOR, FUEL INJECTION, BLOWERS, OR

# NITROUS OXIDE INJECTION.

TIRES:         MAX SIZE 31X15.50X15. ANY PRICE OR BRAND OF TIRE.

# WIDTH OF TIRES MOUNTED ON TRACTOR CANNOT EXCEED

60” ACROSS BACK.

# THROTTLE: MUST BE SPRING LOADED (DEADMAN) THROTTLE.

# DRIVES:    MODIFICATIONS AS NEEDED ( NO 4WD)

# HITCHES:  MUST NOT BE OVER 13” FROM GROUND. HITCH HOLE SHOULD

# BE 1 ½ INCHES ROUND. NO CLEVISES. HITCH MUST BE RIGID AND

NOT MOVE SIDE TO SIDE OR UP AND DOWN. ANY EXTRA HITCH

HOLES MUST BE PLUGGED OFF AT PULL TIME SO SLED CAN BE

HOOKED IN CORRECT HOLE.

# WHEELIE BARS: TRACTOR SHOULD BE EQUIPPED WITH WHEELIE BARS

# STRONG ENOUGH TO SUPPORT TRACTOR AND DRIVER WITH

REAR WHEELS OFF GROUND. BARS SHOULD BE AT LEAST 6”

FROM OUTERMOST PART OF TIRE, BUT NOT MORE THAN 6”

OFF THE GROUND, NO PORTION OF WHEELIE BARS OR TRACTOR

SHOULD TOUCH CHAIN WHEN CHAIN IS TIGHT.

# FRAME:    ALTERATIONS ARE ALLOWED. WHEELBASE NOT TO EXCEED 60”

# CENTER TO CENTER. 8 FEET TOTAL LENGTH FROM REAR OF

BACK TIRE TO FRONT OF TRACTOR. THIS INCLUDES GRILL,

WEIGHTS OR WEIGHT BARS. WHEELIE BARS ARE NOT INCLUDED

IN THIS MEASUREMENT.

# NOTE:       IN THIS CLASS YOU MAY USE A TRANSMISSION OR REAREND

# THAT IS NOT A LAWN & GARDEN TYPE, BUT KEEP IN MIND THE

WEIGHT OF THESE ITEMS MAY BE TOO MUCH ON THE FINISHED

TRACTOR.

# HOOD & GRILL: OPTIONAL, MAY BE FABRICATED. ALL MOVING PARTS

# SHOULD BE COVERED.

# SAFETY SWITCH: TRACTOR SHOULD BE EQUIPPED WITH A BREAKAWAY

# KILL SWITCH.

# FIRE EXTINGUISHER: MUST BE MOUNTED ON TRACTOR.

# AGE:        16 YEARS OLD AND UP